Sail Trim Notes

Question for you racers out there... Going upwind, how close to the centerline do you place the boom before starting to work on the other mainsail controls for optimum speed and pointing? Do you initially position the boom right on or just off the centerline or considerably eased from that position?

> Mike

Typically, I put the boom on centerline unless the wind is very strong and I really need to de-power the main.  Only then will I ask for the traveler to be dropped to put the boom below center.

I've found with the C-320 (unlike the C-30), we are better off reducing the headsail first before reefing the main.  With the C-30, the main gets reefed before the genoa is reduced (The top two boats in the 2000 C-30 Nationals ran the entire regatta in 20 - 25 knots of wind with a full 155% genoa and a single reef in the main (the second place boat on

two starts had a double reef in the main, and that accounted for the difference), while a C-320 on the same course with a 5 min head start start raced with a full main and a storm jib.  As expected, the C-320 beat the C-30s, but he was so far in front that he was difficult to see. Darn you Tomfoolery)

When the wind is very strong, I have my main trimmer bring the traveler up and drop the boom to center to induce twist at the top of the sail and spill a little air.  I also bring the Genoa cars back to do the same thing with the genoa.  I also honk on the backstay adjuster to remove sag from the headstay and flatten the genoa a bit.  Seems to work, I do fairly well.

Steve

Alchemist C-30T #4764, Alchemist C-320 #909

My thought is that unless you really need to go in a certain direction (i.e., very close to the wind), you will never have to use the traveler at any setting but centered. Am I right or is there some other compelling reason to use it? Maybe I'm just lazy, and don't race.

CRA

Rosebud #882

Hi Mike, assuming the mainsheet was already trimmed in hard from the previous tack the traveler we would leave the traveler slightly down from centerline as the Jib Trimmer brings in the big155 Genoa. As the Genoa comes in we would then head up until in a

closehauled position. At that time the boom would be just slightly off thecenterline of the boat. Seems to work OK,

> Joe Barrett

I used to race and we did use the traveler often.  But that was in the last century.  As a lazy day sailor, I almost never touch it, except:

- very close hauled in light air, I pull it to windward a few inches so that the boom is about on center.  Most boats are pretty sensitive to trim in light air so you can easily experiment with the sail controls and find what works.

- if the wind is moderate, say 10 - 12 kts, almost any attempt at sail trim works pretty well (for us day sailors).  I usually don't touch the traveler. Close hauled, I trim the main so that the top batten is more or less on the centerline.  Off the wind, I ease it down a little, unless I forget to. I fiddle with the jib car position, too, unless I forget to do that also.

- if the wind is stronger, say 14 - 15 or so, I ease the traveler to keep the boat so that it heels less.  Most experts say you want to keep the boat to a 15 degree heel angle.  In practice, that's hard if the wind is up

- when to go to Catalina, you will often find that the wind picks up when you are about 6 miles from the island.  When it is blowing about 14-15 kts in mid channel, it can be 18-20 closer to the island.  The autopilot won't hold the course, you'll be tired, your crew will be

complaining about the "lean", and so the thing to do is let the traveler down, maybe even all the way

- we had one trip when the wind was steady in the low 20's mid channel and in the 25-27 kt range near the island.  The wind angle was about 120 degrees.  By reefing the main, pulling in a few turns on the jib furler, and moving the traveler all the way down, the heel reduced to under 20 degrees, the boat speed was still at 7 and we were comfortable.  It feels great to come roaring into the island that way!

- returning from the island the wind will be 110-120 degrees for much of the way. Easing the traveler gives you a more comfortable (level) ride, it's easier on the autopilot, it's at least as fast, and if the line is long enough you can reach it while relaxing on the rail next to the wheel.

> Pete

As an additional thought, I have found that the 320 is very responsive at 18-20 knots of wind to flattening the main by cranking on the outhaul and down on the cunningham. These adjustments are quick, easy and rarely require further spilling of the main by reefing or dumping the sheet. And then only if it is gusty and you are getting puffs in the mid twenties.

I only have a 135 so it does not require furling until above 22.

This technique lets me sail flat, fast and close on the wind below 20. The AP set to the wind is pretty slick in these conditions as well.

With the 135, I have found it better to reef the main above 20 than furl. I am looking for a good blade for those 25-35 days and likely will put in a second reef on the main.

Chris Burti